## Slide 1: Natural gas v alternative routes for production of chemicals in 2022
Abhinandan Nabera
28. October 2022
Institute for Chemical and Bioengineering
Sustainable Process Systems Engineering Lab

## Slide 2: Natural gas prices have increased sharply
Aftermath of COVID-19
Soaring inflation
Climate change
War on Ukraine

## Slide 3: Natural gas contributes around 20.5% towards the electricity mix…
As of 2021, 20.5% of the electricity comes from natural gas in the EU.
Electricity prices have also increased sharply following a similar trend.

## Slide 4: As a result, ammonia production from natural gas (BAU) has become expensive…
1 kg of ammonia requires 0.43 kg of NG as feedstock and 0.10 kg of NG for heating
Also, 1 kg of ammonia requires 0.94 kWh of electricity

## Slide 5: Also, methanol production from natural gas (BAU) has become uneconomical…
1 kg of methanol requires 0.61 kg of NG as feedstock and 0.05 kg of NG for heating
Also, 1 kg of methanol requires 0.71 kWh of electricity

## Slide 6: Model validation

## Slide 7: Green ammonia is more feasible in the current scenario economically…
LCOE values for solar and wind obtained from IRENA for the respective years
LCOH values calculated
LCOH values for nuclear and biomass obtained from Parkinson and adjusted for inflation

## Slide 8: Green ammonia is more feasible in the current scenario economically…
Renewable electricity is only used for the electrolyzer and the electricity mix is used for the process itself
The process consumes 0.47 kWh of electricity per kg of ammonia

## Slide 9: Green ammonia is feasible not only at the peak of natural gas prices

## Slide 10: Green methanol is competitive in the current scenario
Carbon dioxide from DAC
Carbon dioxide itself requires 0.11 kg of NG per kg
The process consumes 0.17 kWh of electricity per kg of methanol

## Slide 11: Green methanol is feasible not only at the peak of natural gas prices

## Slide 12: Save money by using green routes
P.C – cost of production [$ t-1 product]
alt – alternate route
GWP – global warming potential [tCO2eq t-1 product]

## Slide 13: Green hydrogen

## Slide 14: Green hydrogen avoidance costs